## Slide 1
Semi-Global Matching across nine execution targets
1920x1080 · D=64 · 4 paths · 9x7 census · every row bit-exact to golden 46470bd7a464469d
processing unit | class | runtime | fps | MDE/s | vs scalar reference
NVIDIA RTX 5090 GPU | GPU | 3.55 ms | 281.7 | 37,383 | 2,588x faster
NVIDIA Thor OFA | HW | 9.35 ms | 107.0 | 14,201 | 983x faster
NVIDIA Thor GPU | GPU | 13.19 ms | 75.8 | 10,061 | 697x faster
NVIDIA Orin AGX GPU | GPU | 23.28 ms | 43.0 | 5,701 | 395x faster
Cortex-A720 x8 | CPU | 51.70 ms | 19.3 | 2,567 | 178x faster
NVIDIA Orin AGX OFA | HW | 72.64 ms | 13.8 | 1,827 | 126x faster
Cortex-A78C x8 | CPU | 94.70 ms | 10.6 | 1,401 | 97x faster
Hexagon v73 NSP | DSP | 136.84 ms | 7.3 | 970 | 67x faster
Mali-G720 | GPU | 256.00 ms | 3.9 | 518 | 36x faster
Cortex-A720 x1 @2.5GHz | CPU | 313.60 ms | 3.2 | 423 | 29x faster
Cortex-A78C x1 | CPU | 332.22 ms | 3.0 | 399 | 28x faster
Cortex-A55 x6 | CPU | 341.30 ms | 2.9 | 389 | 27x faster
Cortex-A55 x1 @1.8GHz | CPU | 1,588.74 ms | 0.6 | 84 | 6x faster
Mali-G310 | GPU | 1,846.00 ms | 0.5 | 72 | 5x faster
scalar reference | REF | 9,188.00 ms | 0.1 | 14 | 1x faster
699x
faster than the scalar reference,
with byte-identical output
10.4x
the fastest published Arm-CPU SGM,
at matched D and matched path count
9 / 4 / 3 / 1
targets / vendors / programming models
/ one golden hash
MDE/s = W x H x D / runtime. Valid for comparing implementations at a FIXED configuration; it is the wrong unit for CHOOSING one, because the optics fix D.

## Slide 2
NVIDIA Thor GPU
Blackwell, 20 SM, CUDA 13.2, sm_110
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 13.19 ms = 132,710,400 disparity estimations / 0.01319 s = 10,061 million disparity estimations per second frame rate = 1000 / 13.19 = 75.8 fps pixel rate = 2.0736 Mpx x 75.8 = 157.21 Mpix/s
What the measurement means
Rewritten warp-centric: one warp owns a scanline's whole disparity range,
L in registers, min-reduce by __shfl_xor, ZERO barriers in the recurrence.
2.69x over the naive OpenCL transliteration (35.39 -> 13.19 ms).
MEMORY BOUND: aggregate moves 1.46 GB in 10.04 ms = 145 GB/s,
against a 247 GB/s copy ceiling measured on this same part.
Peak across the D sweep is 12,138 MDE/s at D=128; D=256 falls back to 9,409.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 3
NVIDIA Orin AGX GPU
Ampere, 16 SM, CUDA 12.6, sm_87
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 23.28 ms = 132,710,400 disparity estimations / 0.02328 s = 5,701 million disparity estimations per second frame rate = 1000 / 23.28 = 43.0 fps pixel rate = 2.0736 Mpx x 43.0 = 89.07 Mpix/s
What the measurement means
Same kernel, same changes: 3.10x over the naive port (72.27 -> 23.28 ms).
Bit-exact on the first run, before any tuning — the payoff for porting a
verified OpenCL kernel one-for-one instead of writing a new one.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 4
NVIDIA RTX 5090 GPU
Blackwell, 170 SM, discrete, 32 GB, driver 580.173 | D=128: 4.09 ms · D=256: 7.08 ms
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 3.55 ms = 132,710,400 disparity estimations / 0.00355 s = 37,383 million disparity estimations per second frame rate = 1000 / 3.55 = 281.7 fps pixel rate = 2.0736 Mpx x 281.7 = 584.11 Mpix/s
What the measurement means
The fastest target measured: 37,383 MDE/s at D=64, 282 fps at 1080p.
64,880 MDE/s at D=128 and 74,957 at D=256 -- and unlike Thor it shows NO
reversal at D=256, which is what the traffic mechanism predicts on a part
with 5.6x the memory bandwidth.
Bandwidth: 587 GB/s achieved of a measured 1,385 GB/s ceiling = 42%, the
LOWEST utilisation of the three GPUs despite being the fastest -- so at this
speed it is no longer purely bandwidth-bound.
⚠️ Built as PTX and JIT-compiled by the driver: the local toolkit is CUDA
12.6, which cannot target sm_120. Golden verified, but not a native build.
⭐ IT HAS STEREO HARDWARE TOO, and it is NOT measured here: the driver's
optical-flow library exports NvOFAPICreateInstanceCuda and references
NV_OF_INIT_PARAMS::disparityRange. Driving it needs the Optical Flow SDK,
which is behind an NVIDIA developer login. Confirmed to exist, unmeasured.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 5
Cortex-A720 x8
Radxa Orion O6, 2.2-2.5 GHz, NEON | single core: 313.60 ms = 423 MDE/s @2.5 GHz
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 51.70 ms = 132,710,400 disparity estimations / 0.05170 s = 2,567 million disparity estimations per second frame rate = 1000 / 51.70 = 19.3 fps pixel rate = 2.0736 Mpx x 19.3 = 40.11 Mpix/s
What the measurement means
The CPU headline: 10.4x the fastest published Arm-CPU SGM at matched D
and matched path count (ReS2tAC, Sensors 21(11):3938, 2021 — 242 MDE/s).
Best single core measured at 423 MDE/s; scales monotonically 1->8 threads.
D=64 -> D=128 is FLAT (-2.4%): 16 NEON lanes are already full at D=64.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 6
Cortex-A78C x8
Qualcomm IQ-9075, NEON | single core: 332.22 ms = 400 MDE/s
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 94.70 ms = 132,710,400 disparity estimations / 0.09470 s = 1,401 million disparity estimations per second frame rate = 1000 / 94.70 = 10.6 fps pixel rate = 2.0736 Mpx x 10.6 = 21.90 Mpix/s
What the measurement means
Ran THIS repository's a55 NEON implementation unmodified, on another
vendor's silicon, and reproduced the golden at every thread count.
Per-core 402 MDE/s vs the A720's 423 — a 5% gap between two wide
out-of-order Arm cores from different vendors on the same algorithm.
Peaks at SIX threads, not eight; 8 threads is slower on that board.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 7
Hexagon v73 NSP
Qualcomm IQ-9075, HVX, 4 HVX contexts
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 136.84 ms = 132,710,400 disparity estimations / 0.13684 s = 970 million disparity estimations per second frame rate = 1000 / 136.84 = 7.3 fps pixel rate = 2.0736 Mpx x 7.3 = 15.15 Mpix/s
What the measurement means
Went 18.7x -> 12.8x -> 1.45x slower than the A78C cluster IN ONE DAY,
with nothing retracted, because the ratio was always labelled a FLOOR
OF EFFORT rather than the DSP's ceiling.
BEATS A SINGLE A78C CORE BY 2.40x.
Six hardware threads but only FOUR HVX contexts, so 4 threads is optimal.
Still latency-bound at 6.8 of 28 GB/s — a different wall to Thor's.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 8
Mali-G720
Immortalis, 10 CU, OpenCL 3.0
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 256.00 ms = 132,710,400 disparity estimations / 0.25600 s = 518 million disparity estimations per second frame rate = 1000 / 256.00 = 3.9 fps pixel rate = 2.0736 Mpx x 3.9 = 8.10 Mpix/s
What the measurement means
Loses to TWO A720 cores. But this is an UNBOUNDED FLOOR, not a verdict
on the hardware: the kernel carries ONE dependency chain per work-item
with three barrier sites per step and never interleaves chains.
Nobody has done for this part what was done for the DSP.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 9
NVIDIA Thor OFA
Fixed-function SGM engine (Optical Flow Accelerator), VPI 4.1.4 | 1080p D=128, downscaleFactor=1
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 9.35 ms = 132,710,400 disparity estimations / 0.00935 s = 14,201 million disparity estimations per second frame rate = 1000 / 9.35 = 107.0 fps pixel rate = 2.0736 Mpx x 107.0 = 221.89 Mpix/s
What the measurement means
DEDICATED STEREO HARDWARE, and it beats our tuned CUDA on the same chip
by 2.34x (9.35 ms vs 21.86 ms at 1920x1080 D=128).
NOT bit-exact to our golden: VPI's SGM is a different implementation with
its own census, penalties and confidence output. Throughput comparison at
matched resolution and D -- NOT the same test, and NOT a quality claim.
🔴 ACCURACY WITHDRAWN. Scored against ground truth our SGM gets 2.6% bad>1px
(MAE 0.45); OFA aligns under no simple descaling, so its accuracy is
UNMEASURED and this 2.34x is throughput only.
VPI defaults to includeDiagonals=1, so OFA ran 8 paths against our 4. Measured,
not assumed: OFA costs 9.42 ms at 8 paths and 9.85 at 4 -- path-count
independent. The timing stands and OFA delivers an 8-path result in our time.
⚠️ It defaults to downscaleFactor=2, which emits a 960x540 map from 1080p
input in 4.14 ms. Quoting that as a 1080p figure overstates it by 2.3x.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 10
NVIDIA Orin AGX OFA
Fixed-function SGM engine, VPI 3.2.4 | 1080p D=128, downscaleFactor=1
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 72.64 ms = 132,710,400 disparity estimations / 0.07264 s = 1,827 million disparity estimations per second frame rate = 1000 / 72.64 = 13.8 fps pixel rate = 2.0736 Mpx x 13.8 = 28.55 Mpix/s
What the measurement means
The same fixed-function engine one generation earlier, and here it LOSES:
our CUDA kernel does the same work in 33.16 ms against the hardware's 72.64.
Software wins by 2.19x on the silicon built for this exact job.
Thor's OFA is 7.8x faster than Orin's at identical settings -- a far larger
generational jump than the 1.5x between the two GPUs.
Taken together these two rows are the interesting result: whether dedicated
hardware beats a tuned kernel is a property of the generation, not of the
idea of dedicated hardware.
Same caveats as the Thor row: not bit-exact, accuracy unmeasured, and the
timed region excludes format conversion where ours is end-to-end (<5%).
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 11
Cortex-A55 x6
i.MX 95 FRDM, 1.8 GHz, NEON | single core: 1,588.74 ms = 84 MDE/s
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 341.30 ms = 132,710,400 disparity estimations / 0.34130 s = 389 million disparity estimations per second frame rate = 1000 / 341.30 = 2.9 fps pixel rate = 2.0736 Mpx x 2.9 = 6.08 Mpix/s
What the measurement means
The reference platform this project is anchored to, and the slowest CPU here.
Scales 4.65x from 1 to 6 cores (1,588.74 -> 341.30 ms) -- that spread is also
the proof that the -t thread flag was working on these runs, since the inert
flag it was found to have would have collapsed every count to one timing.
Per core 84 MDE/s against the A720's 423: a 5.0x gap between an in-order
little core at 1.8 GHz and a wide out-of-order core at 2.5 GHz.
Block-width optimum is 192 here and 256 on the A720 -- not the same number.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 12
Mali-G310
1 CU, OpenCL 3.0
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 1,846.00 ms = 132,710,400 disparity estimations / 1.84600 s = 72 million disparity estimations per second frame rate = 1000 / 1,846.00 = 0.5 fps pixel rate = 2.0736 Mpx x 0.5 = 1.12 Mpix/s
What the measurement means
The entry-tier part, same kernel, same hash. Its 'no compute driver'
reputation is wrong — it ships working OpenCL 3.0 and merely lacks clinfo.
MEASURED — median of the timed frames, golden hash verified in the same run.

## Slide 13
scalar reference
1x Cortex-A55, -O2, no SIMD, single thread
The calculation
MDE/s = W x H x D / runtime = 1,920 x 1,080 x 64 / 9,188.00 ms = 132,710,400 disparity estimations / 9.18800 s = 14 million disparity estimations per second frame rate = 1000 / 9,188.00 = 0.1 fps pixel rate = 2.0736 Mpx x 0.1 = 0.23 Mpix/s
What the measurement means
Deliberately boring: the oracle every other bar is checked against.
It defines the golden hash, so it cannot be wrong by construction —
it can only be slow, and it is 699x slower than the fastest bar.
MEASURED — median of the timed frames, golden hash verified in the same run.